## Slide 1
Systems Design for the
GEOSAIL Solar Sail Mission
Vaios Lappas(1), Giovanni Mengali(2), Alessandro Quarta(3), Jesus Gil-Fernandez(4), Tilo Schmidt(5), Bong Wie(6)
(1) University of Surrey, E-mail: V.Lappas@surrey.ac.uk,
(2) University of Pisa, E-mail: g.mengali@ing.unipi.it
(3) University of Pisa, E-mail: a.quarta@ing.unipi.it
(4) GMV, Madrid, Spain, E-mail: jesusgil@gmv.es
(5) HTS, E-mail: tilo.schmidt@htsdd.de
(6) Iowa State University, USA, E-mail: bong.wie@isu.edu

## Slide 2
  ESA Technology Reference Missions
  Mission Requirements
  Mission Analysis
  Payloads
  Solar Sail Steering Law
  Solar Sail Design
  Satellite Bus
  ADCS
  Mass/Power Budgets
  Conclusion
Contents

## Slide 3
  Recent advances in solar sail technologies, satellite bus miniaturisation and attitude control make necessary revisiting the design of GEOSAIL with a more realistic and hopeful perspective.
  Technology Reference Studies (TRS) have been introduced by the European Space Agency (ESA) to focus on the development of strategically important technologies in preparation of future scientific missions.
  A number of TRS have been successfully studied in the context of ESA’s scientific Cosmic Vision 2015-2025
  Among many Solar Sail mission concepts (Solar Probe, Interstellar Probe), GEOSAIL has been identified by ESA’s Science Payload and Advanced Concept Office as a potential future ESA scientific mission.
ESA Technology Reference Missions

## Slide 4
  A 40 x 40 m solar sail can be used to artificially precess the apse-line of 11 x 23 Earth radii orbit, stationing a miniature science payload permanently within the geomagnetic tail and so providing continuous science returns.
  The permanent residence of the payload in the geomagnetic tail would allow phenomena such as magnetic reconnection to be studied in-situ.
  Using a single or multiple solar sails, the entire geomagnetic tail could be populated by sensors that precess with the annual rotation of the geomagnetic tail, allowing real-time visualisation of the 3D plasma structure of the geomagnetic tail.
GEOSAIL: The Mission*
*Reference: McInnes, C. R., Macdonald, M., Angelopoulos, V., and Alexander, D., “GEOSAIL: Exploring the Geomagnetic Tail Using a Small Solar Sail,” Journal of Spacecraft and Rockets, Vol. 38, No. 4, July-August 2001, pp. 622–629.

## Slide 5
  Conventional geomagnetic tail missions require a spacecraft to be injected into a long elliptical orbit to explore the length of the geomagnetic tail.
  However, since the orbit is inertially fixed, and the geomagnetic tail points along the Sun-Earth line, the apse line of the orbit is precisely aligned with the geomagnetic tail only once every year.
  Approximately 4 months of data can be acquired, with only 1 month of accurate data from the tail axis.
  To artificially precess the apse line of the elliptical orbit to keep the spacecraft in the geomagnetic tail during the entire year would be prohibitive using chemical propulsion.
  A scientifically interesting 11 x 23 Earth radii (RE) elliptical orbit would require a of order 3.5 km/s per year of operation for apse line rotation.
  Although the for apse line rotation is large, only a small acceleration continuously directed along the apse line is required
GEOSAIL: The Mission (II)

## Slide 6
  The aim of this GEOSAIL study is to establish a cost-efficient and technologically feasible mission architecture for a solar sailing Earth magnetosphere exploration mission
  Emphasis on the specific system design of the spacecraft and sail.
  Analyse the feasibility of a practical, realistic, low cost GEOSAIL solar sail mission based on the ‘small satellite paradigm’
  Analyse critical and mission enhancing technologies
    Eject-able sail deployment module
    ADCS
    Small Satellite Bus
    Use of COTS
    Transfer trajectory trade-off to the GEOSAIL orbit
Aims

## Slide 7
GEOSAIL Mission Requirements*

## Slide 8
GEOSAIL Mission Requirements*
* Science Payload and Advanced Concept Office, “Executive Summary of the GEOSAIL Study,” document SCI-A/2006/005/GS, European Space Agency, April 2006

## Slide 9
  The science objectives for GEOSAIL are to investigate the occurrence of magnetic reconnection in the magnetotail plasma sheet, to investigate reconnection processes at the sub-solar point, and to investigate the magnetospheric boundary layer
  GEOSAIL ability to maintain it's apogee in the geo-tail against the natural precession relative to the Sun-Earth line imposed by the Earth's orbital motion means that GEOSAIL will be able to study systematically the seasonal influences on the reconnection processes, especially in the geomagnetic tail.
  Seasonal variations arise because the near-Earth portion (< 10 RE) of the tail is influenced by the tilt of the Earth's magnetic dipole (11 degrees) in addition to the tilt of the geographic rotation axis (23 degrees).
  These effects give rise to a daily flapping motion of the tail with respect to the ecliptic plane, and another one, which is different in different seasons.
Science Objectives

## Slide 10
Payload

## Slide 11
  Given the operational orbit (1123 RE with two different inclinations, 90º and 23.5º) and considering also the launcher requirement (VEGA or similar low-cost launcher), several possibilities exist to reach the final orbit, as, for example:
  Solar Sail + Chemical Propulsion (SS+CP), where the transfer from the launcher injection orbit to the operational orbit is done with the CP via high-thrust manoeuvres
  (ii) Solar Sail + Electric Propulsion (SS+EP), where the EP provides the thrust during the multi-revolution transfer and
  (iii) Dedicated Solar Sail (SS) in which no additional propulsion system (apart from the sail) is mounted and the SS provides the continuous thrust for the transfer
Mission Analysis: Trajectory/Transfer

## Slide 12
Transfer : Propulsion Trade-Off

## Slide 13
  For transfer design the baseline is a VEGA launcher that injects the SC into a 23º inclination circular orbit
  the total target mass into operational orbit is 172 kg (85 kg sail + 87 kg satellite bus), which is used as a design assumption
  A constant maximum thrust at 85.5 mN and specific impulse ISP = 1650s based on the SMART-1 Snecma PPS-1350 thruster are used.
  An initial spacecraft mass (including the transfer module) of 500 kg is used, including 20% margin,
  The propellant is 200 kg and the mass of engines, tanks, valves, pipes and power control is estimated from Snecma data to 65 kg if 2 engines and 4 tanks are used (with only 1 engine the transfer can still be carried out but with an approximately doubled flight time
  Chemical: An EADS 400N Bipropellant thruster is used (model S400-2) which provides a 400 N thrust at 318 s Isp
Transfer Propulsion Assumptions

## Slide 14
Launch and Transfer Performance

## Slide 15
Chemical Multi-Burn Transfer

## Slide 16
Minimum Time EP Transfer

## Slide 17
Propellant Budget

## Slide 18
  Assuming an ideal solar sail model, McInnes et al. have proposed a simple steering law that consists in orienting the sail in such a way that its normal is always directed along the Sun-sail line (the latter, in turn, coincides with the orbit apse-line).
  A new enhanced steering law is used that takes into account the shadowing effects due to the eclipse periods which is important for the sailcraft design as these key factors have a direct impact on the sail characteristic acceleration requirement
  where b1 and b2 are the optical coefficients, α is the characteristic acceleration of the solar sail and is the shadow function fs according to whether the solar sail is in umbra, in sunlight or in penumbra
  The developed optimal steering law allows one to suitably trade-off between the conflicting requirements of maximizing the apse-line precession capability and the control effort required to achieve that precession
GEOSAIL Steering Law

## Slide 19
In mathematical terms, the problem can be presented into that of maximizing the functional defined as:
  where ω =ω(tf) and subscript f stands for final, that is, after a whole orbital period.
  The trade-off between sail precession effectiveness and control effort is accomplished through the value of parameter η , which may range between 0 and 1.
  Values of η close to 0 correspond to “small” variations allowed for the pitch angle, whereas, as long as η is increased, more control energy may be employed, thus increasing the solar sail precession efficiency
GEOSAIL Steering Law

## Slide 20
Sail performance as a function of η for different values of αc
Condition: The rotation of the apse-line of the GEOSAIL orbit needs to be synchronous with the rotation of the Sun-line, ie the identity:

## Slide 21
Optimal steering law and variation of ω over one orbit (η = 1)

## Slide 22
Sail performance as a function of αc
Assuming η = 1, the minimum admissible value of the characteristic acceleration is αc = 1.1 αc-des = 1.06 mm/s2, a value close to that previously estimated by neglecting the variation of orbit eccentricity and semi-major
axis length.

## Slide 23
  The steering law used takes into account all of the fundamental effects influencing the sail performance capabilities, including the shadowing effects due to the eclipse periods which is usually never accounted for in solar sail design.
  A linear relationship between the solar sail characteristic acceleration and the apse-line precession rate has been shown to exist, thus allowing for a simple estimate of the minimum value of αc necessary to perform the
  GEOSAIL mission.
  This value may then be increased by a reasonable safety margin to
  compensate for the optical characteristic degradation of the sail due to a long stay in a hostile environment.
  The optimal steering law provides a small but significant performance
  improvement with respect to simply orienting, at all time, the solar sail plane normal to the Sun-sail line.
  This finding is a key design feature used for the GEOSAIL solar sail sizing and design.
New Steering Law Benefits*
*Mengali, G., Quarta, A., Lappas, V., ”Optimal Steering Law for the GeoSail Mission,” Journal of Guidance, Dynamics and Control, Vol. 30, No. 3, May–June 2007, pp. 876-879.

## Slide 24
Solar Sail: In-Orbit Bonding
  The proposed GEOSAIL design is based on the In Orbit Bonding (IOB) design, which provides an advantageous solution for both sail boom requirements.
  The IOB technology uses similar boom cross sections, but shifts the assembling process into orbit.
  The storage of two semi-finished half sections allows compact storage, a design feature critical for solar sails.
  During deployment the boom halves are to be aligned to each other adhesively bonded.
  With the possibility of varying shell thickness or cross section size a design close to the load conditions becomes feasible which optimises the structure with respect to mass requirements.
  Considering that the sail deployment is a one shot process the majority of mechanical and structural components used for this will no longer be needed afterwards.
  The IOB sail design allows jettisoning of this mass fraction after reaching its desired size, thus substantially reducing the sail mass

## Slide 25
Solar Sail: In-Orbit Bonding

## Slide 26
Sail Configuration/Design Req’s

## Slide 27
Sail Configuration

## Slide 28
Sail Layout Configuration

## Slide 29
  There is a need to develop an efficient, scalable ACS with the optional possibility of decoupling the ACS from the sail booms adding design flexibility and simplicity to the sail design.
  The design proposed for GEOSAIL is a spacecraft bus-oriented ACS system decoupled from the sail.
  Although challenging due to the large and persistent SRP disturbance leading to excessive angular momentum build up, the proposed ACS system enables a compact and robust control scheme using flight proven technologies with minimum risk and scalability
  A trim-ballast system based on four 10-m booms with 2 kg ballast masses used to trim the sail and allow attitude control with micro reaction wheels
  The booms are also used to place miniature micro Plasma Pulsed Thruster (PPT).
  The large torque arms are used to maximise the effectiveness of the small forces produced by the PPT thrusters.
ADCS Bus Based Scheme

## Slide 30
ADCS Bus Based Scheme

## Slide 31
ADCS Bus Based Scheme

## Slide 32
20 Deg Simulation: Roll Axis

## Slide 33
20 Deg Simulation: Pitch Axis

## Slide 34
20 Deg Simulation: Yaw Axis

## Slide 35
  The core structure is a standard Surrey small satellite modular, self-supporting stack of equipment boxes.
  Each module box carries one or more subsystems, serving as both
  subsystem enclosure and structural element.
  The top facet is the interface with the solar sail module.
  This is surrounded by shear panels, which connect and transfer the loads from the stack to the facet, and to which, non-structural “mini-stacks” of “nanotrays” are bolted.
  These nanotrays represent the next step in miniaturisation, and are a direct result of the work done on developing, smaller, more efficient subsystems, demonstrated on the SNAP-1 nanosatellite.
Satellite Bus

## Slide 36
RF Subsystem: S-Band

## Slide 37
Power Subsystem

## Slide 38
GEOSAIL Bus Mass/Power Budget

## Slide 39
Conclusion (I)
  GEOSAIL is proposed as a low cost solar sail mission to study the Earth’s magneto-tail.
  Due to ΔV restrictions, missions using conventional propulsion systems can only remain in the Earth’s magneto-tail region for a limited time (about 3 months/yr).
  A trade-off for the sail trajectory transfer to its 11 x 23 Earth radii elliptical orbit for a combined sail and chemical design versus a sail and electric propulsion design examined the mass and time issue for getting the solar sail to its operational orbit.
  Due to mass constraints the electric propulsion design based on the SMART-1 architecture was selected as the baseline option leading to a 250.7 kg mass design for the transfer vehicle.
  A new sail steering law taking into consideration the sail degradation effects and eclipses is used to design the solar sail subsystem.
  For the sail design, the IOB technique is used to deploy efficiently lightweight
  rigidizable booms.

## Slide 40
  The proposed IOB design, which has been tested in laboratory experiments on the ground, comes with the inherent design feature of in-space jettison of all used and unnecessary components after sail deployment, thus significantly reducing mass.
  Different sail configurations and designs were traded off against each other leading to a practical, realistic design with an after jettison mass of 44.4 kg.
  A bus based ACS subsystem is proposed combining a trim-ballast system with a PPT low cost propulsion system used as back up providing robust attitude control.
  The sail bus uses COTS based subsystems derived from small satellite heritage leading to significant mass savings for a 85 kg bus with peak and average power requirements of 88 and 56.1 W respectively, well within existing small capabilities.
  Total Solar Sail spacecraft Mass (44.4 + 85 + 250.7) = 380.1 kg after jettison
      Launch Mass = 407.4 kg
Conclusion (II)*
* Lappas, V., Mengali, G., Quarta, Q., Gil-Fernandez, G.,
Schmidt, T., Wie, B., ‘Systems Design for the GEOSAIL Solar Sail Mission’, Submitted to Journal of Spacecraft and Rockets