## Slide 1
Bernd Dachwald
German Aerospace Center (DLR) Mission Operations Section Oberpfaffenhofen
bernd.dachwald@dlr.de
Global Optimization of Solar Sail Trajectories Using Evolutionary Neurocontrol: New Results
1st International Symposium on Solar Sailing, 27-29 June 2007, Herrsching, Germany

## Slide 2: Trajectory Optimization for Spacecraft with Continuous Thrust
F0 = ?
F2 = F2 (F0)
F0 = ?
F1 = ?
F2 = ?
F3 = ?
F4 = ?
F5 = ?
F6 = ?
F7 = ?
F8 = ?
F9 = ?
F10 = ?
F11 = ?
Fn = ?
trajectory of
launch body
trajectory of
target body
spacecraft
trajectory
Continuous thrust makes trajectory optimization difficult !
F1 = F1 (F0)
Impulsive-Thrust Trajectory Continuous-Thrust Trajectory

## Slide 3: Solar Sail Trajectory Optimization
x (t)
trajectory
equations of motion
solar sail control function
u(t)  n (t)
optimality w.r.t. trip time (or other objective), described by cost function J, which is subject to minimization
solar sail control history
u[t]  n[t]
discretization

## Slide 4: Drawbacks of Local Trajectory Optimization Methods
require an adequate initial guess prior to optimization
  convergence behavior is very sensitive to the initial guess
  similar initial guesses yield often very dissimilar optimization results
    initial guess can not be improved iteratively
    trajectory optimization becomes “more of an art than science”
can only be applied by an expert in astrodynamics and optimal control theory
require frequent interactions with the expert
are often time-consuming (and thus expensive)
run typically into the local optimum which is closest to the initial guess (rarely close to the global optimum)
initial conditions are typically not optimized, although they are crucial for mission performance

## Slide 5: Smart Global Trajectory Optimization
global trajectory optimizer
choose initial conditions
near-globally optimal trajectory found
choose target body
interval for launch time interval for hyperbolic excess velocity
Artificial Neural Network
Evolutionary Neurocontroller (ENC)
Evolutionary
Algorithm

## Slide 6: The Flight Control System of the Housefly:
housefly steering
etc. etc. etc.
evolution
neural network
 100 000 neurons
evolutionary neurocontroller
neurocontroller
optimizes
performs
a natural evolutionary neurocontroller (ENC)
Notes: Animal nervous systems incorporate natural evolutionary neurocontrollers to control their actions, giving them marvelous capabilities.
One brilliant example for this proposition is the smart flight control system of the housefly. The nervous system of the housefly comprises about 100 000 neurons. This natural neural network manages the flight control of the fly as well as many even more difficult tasks like finding food, finding a mate, producing offspring, etc. As a matter of fact, this flight control system is more ingenious than the one of any aircraft man has ever built. Nature has optimized the fly’s neurocontroller with respect to one single objective: survive to produce offspring. This optimization problem is really very difficult, much more than finding some optimal spacecraft trajectory. Nature has solved this problem through the recombination and mutation of the fly’s genetic material and through natural selection, the famous so-called ”survival of the fittest”. Fitter flies produce more offspring and there is a high probability that some of them are still smarter than their parents. This very elegant optimization process runs without an initial guess and without employing the calculus of variations!

## Slide 7: Solar Sail Trajectory Optimization Using Evolutionary Neurocontrol
spacecraft steering
evolutionary algorithm
artificial
neural network
 50 neurons
evolutionary neurocontroller
neurocontroller
optimizes
performs
Notes: So, if a natural evolutionary neurocontroller can steer a housefly optimally from A to B, why should an artificial evolutionary neurocontroller not be able to steer a solar sail optimally from A to B?
We take an artificial neural network and let this neural network perform the steering of the solar sail. Every distinct neural network incorporates an individual steering strategy. To select between the smart and the stupid ones we simply imitate evolution by employing an evolutionary algorithm.

## Slide 8: Artificial Neural Networks
primitive function
internal network parameter
input vector
output vector
x1
x2
x3
x4
y1
y2
this neural network maps a 4D input
space onto a 2D output space
as associative mapping functions
N: X  R4  Y  (0,1)2
network function N, defined by its (constant) internal parameters R28
Notes: Internally, an ANN comprises artificial neurons and artificial synapses that are arranged in layered topology. This example networks gets 4 input values and maps them onto 2 output values. The whole network is defined by 23 internal parameters.
For most practical purposes an artificial neural network can simply be regarded as a black box function. This one is a black box function that maps a 4D input space onto a 2D output space. This network function, is completely defined by the network’s 23 constant internal parameters. Note that the parameters for a given network function are constant. If we change those parameters, e.g. during learning, we get a different network function.

## Slide 9: Combining Artificial Neural Networks and Evolutionary Algorithms
an artificial neural network can be mapped onto a “chromosome“
the artificial neural network that performs best on a given task can be „bred“ with an evolutionary algorithm
chromosome
Notes: The application of an EA to search for the ANN’s optimal network function makes use of the fact that the parameter vector of the ANN can be mapped onto a string, which then provides an equivalent description of the network function. By searching for the fittest string, the EA searches for the ANN’s optimal network function and this way, breeds the optimal ANN.

## Slide 10: Trajectory Optimization Using Evolutionary Neurocontrol
Notes: This slide shows, how a solar sail can be steered using an evolutionary neurocontroller.
To find the optimal solar sail trajectory, the ENC method is running in two loops. Within the (inner) trajectory integration loop, an NC steers the solar sail according to its network function, that is completely defined by the NC’s parameter vector, which is set and evaluated by the EA in the (outer) NC optimization loop. The EA holds a population of NC parameter vectors. Within the trajectory integration loop the EA evaluates all NC parameter vectors for their suitability to generate an optimal trajectory. For that evaluation, within the trajectory optimization loop, the NC takes the actual solar sail state and that of the target body as input values, and maps from them onto some output values. The output values of the neurocontroller are interpreted as the components of the required direction vector. From this, the solar sail normal vector can be calculated. Then, the spacecraft state and control are inserted into the equations of motion, which are numerically integrated over one time step. The new state is fed back into the NC. The trajectory integration loop stops, when the accuracy of the trajectory is sufficient or when some time limit is reached. Then, back in the NC optimization loop, the NC’s parameter vector (i.e. its trajectory) is rated by the EA’s fitness function. Under the selection pressure of the environment, the EA breeds NCs that generate more and more suitable steering strategies that in turn generate better and better trajectories. The EA finally converges against a single steering strategy, which gives in the best case a near-globally optimal trajectory.

## Slide 11: Trajectory Optimization Using Evolutionary Neurocontrol
action
1 life of a fly
perceived environment

## Slide 12: Fast Solar System Escape Trajectories Using “Solar Photonic Assists”
trip time depends on minimal solar distance during the close solar passes (the smaller the solar distance, the larger the energy gain)
the minimal solar distance is limited by the temperature limit of the sail film
however, the sail temperature depends also on sail attitude
trade-off between time that is spend in the inner solar system to gain orbital energy and time / velocity that is required afterwards to fly outwards
this yields complicated trajectories that are very hard to optimize with local optimization methods

## Slide 13: Mission to the Heliopause (200AU)
evidence for near-global optimality of the solutions

## Slide 14: Solar Polar Imager Mission: Reference Solution

## Slide 15: Solar Polar Imager Mission: Hot Szenario
Sail temperature limit: Tlim = 100°C
Hyperbolic excess energy: C3 = 0.25 km2/s2
Characteristic acceleration: ac = 0.35 mm/s2
Mission duration: 6.2 years

## Slide 16: Solar Polar Imager Mission: Hot Szenario
Sail temperature limit: Tlim = 240°C
Hyperbolic excess energy: C3 = 0 km2/s2
Characteristic acceleration: ac = 0.35 mm/s2
Mission duration: 4.7 years

## Slide 17: Mission to Deflect Near-Earth Asteroid Apophis
The highest impact velocity can be achieved from a retrograde orbit.
Using chemical or electric propulsion, too many gravity assists and therefore too much time is required to make a spacecraft trajectory retrograde ( 30 years).
Char. Acceleration: 0.5 mm/s2
Mission duration: 6 years
Impact velocity: 75.4 km/s
The simplest way to deflect a NEO is to impact it with a massive projectile at a high relative velocity.
The solar sail might be the better propulsion system for such a mission.

## Slide 18: Summary and Conclusions
evolutionary neurocontrol (ENC) is able to calculate a wide variety of at least near-globally optimal trajectories
  different low-thrust propulsion systems
  different astrodynamical problems
(co-) optimization of initial conditions is possible
solutions are at least similar, for difficult problems mostly even better than expert-generated solutions (using local trajectory optimization methods)
ENC has – to my knowledge – produced the only near-globally optimal trajectories for the following very difficult problems
  solar system escape with near-term solar sails (with many solar photonic assists)
  the Solar Polar Imager
  a retrograde asteroid deflection mission
ENC requires no initial guess
ENC requires only basic knowledge in astrodynamics and no knowledge in optimal control theory