## Slide 1: GeoSail Environment & Effects

## Slide 2: Contents
What is GeoSail and why is it’s environment interesting?
What is GeoSail orbit environment?
Overview of general space environments & effects
What are GeoSail’s interactions with environment?
Review of environment analysis for GeoSail
Conclusions
Environment comparisons with SPO and IHP missions

## Slide 3: What is GeoSail?
Solar Sailing Demonstration Mission
Science Mission - Continuously explore Earth’s reconnection regions:
  Noon Magnetopause & Magnetosheath
  Magnetotail and Plasma Sheets
  Lobes
~50m diameter square sail
Mast 10m TBD, central cut-out 10m TBD
~11 x 23Re orbit radius, ~4.1 day orbit
Launch 2015-25 Assumed launch 2020 for (‘JPL’ solar max)
2 years sailing, 1 year without sail
GeoSail provides an orbit regression of 1deg/day to keep the orbit apogee permanently in the Earth’s magnetotail (this would require significant propellant using electric or chemical propulsion)
Early conceptual view of GeoSail fully deployed

## Slide 4: Why is GeoSail environment interesting?
Orbit unusual & not well known
  Variable plasma
  >3 hour Eclipses
Spacecraft (pseudo) sun-pointing
Shape unusually large & interacts with & modifies environment:
  Ram/wake effects
  Charging (Differential, High Potentials)
  EMC
Shape may be susceptible to unique environment effects
  Only 3microns thick
  Thermal shocks in/out of eclipse
Can feed into SPO and IHP
Combined GeoSail orbit environment & spacecraft design challenging!

## Slide 5: What is GeoSail’s orbit environment?
Solar Cycle dependencies
  11 year
  27 day
Seasonal dependencies
Solar Eclipses (11x23 Re)
  Penumbra shadow angle = 2.7 deg.
  Penumbra entry to exit = 196.6 min (used for battery sizing)
  Umbra shadow angle = 2.2 deg.
  Umbra entry to exit = 157.1 min
  270 eclipses in 3 years
Lunar Eclipses
GeoSail orbit showing location of tailbox region. Note that tailbox position shifts seasonally crossing the ecliptic at the equinoxes. .

## Slide 6: Overview of General Environments & Effects
ECSS Environments
External
Microgravity
Geomagnetic fields
Solar e-m radiation
Energetic Particles
Plasmas
Micrometeoroids
Contamination
Spacecraft Environment
EMC
Contamination
Environments also act synergystically!

## Slide 7: What are interactions with environment?
Generic environments & effects
  Applicable to normal missions
  Interactions with platform
Specific interactions & effects for GeoSail-type spacecraft including:
  Unique to GeoSail spacecraft
  Interactions with sail/booms
Undisturbed environment directly on the Sail or Platform,
Modulation/disturbance of external environment by Sail & subsequent effects on Platform/Instrumentation
  Platform effects onto sail

## Slide 8: What does this mean?
Mission environment is a primary driver for GeoSail!
Important effects are:
  reflections from sail, eclipses (thermal)
  degradation of sail material integrity (combined environments)
  interference on sensors from sail charging (interaction with plasma)
Need characterisation of many environmental aspects
  thermal loading (inc. spacecraft power) and eclipses
  UV and energetic radiation fluxes,
  micrometeoroid impacts,
  plasma properties (density/energy profiles, surface charging, ram/wake effects),
Very large surface area & lack of in-orbit data - considerable uncertainty to fidelity/applicability of older models.
Better modelling and testing required!

## Slide 9: Thermal Environment
Thermal design must cope with:
  High/low power modes (hot/cold cases)
  With/without sail
  Off-pointing & possible reflections from sail? (much more heat input)
  long eclipses once per orbit (very cold case!)
Complexity requires analysis
Hot case drives:
  radiator design - Limited area!
  Sail design (central cut-out?)
Cold case require heaters
  drives power!
Eclipse of 2.5 hrs

## Slide 10: Thermal Environment
Reflections dependant on sail cut-out size & sail/mast angle to sun
Reflections lead to:
  Increased heat input
  Increased radiator area requirement
  Increased heater power requirement
Specular reflection onto spacecraft at angles >12° for 10m mast/sail cut-out
  Heat input worse beyond 12°
GeoSail platform does not have the area available for increased radiators
  Would require heat shields
Specular reflection from the sail onto the spacecraft must be avoided
  Keeps thermal design low mass
  Need careful choice of mast/cut-out

## Slide 11: Sail Degradation from Environment factors
Probable chronic degradation of sail by combination of environments:-
  Degradation of properties due to UV
  Regular eclipses result in cyclic expansion/contraction stressing of film,
  Embrittlement by radiation; dose rates in thin sail material ~10Mrad/yr
  Occasional perforation events by meteoroids.
Processes/effects still major unknown
Design of film must address this progressive degradation scenario,
  partly by design
  partly by test.
KOBE test-facility at DLR,
  will perform simulated environment of solar-thermal, radiation, UV
  NOT micrometeoroids

## Slide 12: Plasma Environment
Plasma environment in GeoSail orbit is complex & highly variable
  Variable plasma density/velocity
  Eclipses - Solar once/orbit, Lunar (different plasma environment!)
  Not well documented regions
Unusual GeoSail spacecraft will interact with environment – even more complex!
  Unusual sheath - Thick Sheath approximations
  EMC from spacecraft/sail cause payload interference
  Ram/wake effects
  Large Charging area
Main considerations for plasmas
  Debye Length (disturbance range)
  Charging (arcing & science measurements)
Needs modelling!

## Slide 13: Debye Length and Charging
Debye Length, 
  Plasma disturbance range (point source)
  Depends on plasma energy & density
  Requires modifications for large objects
  Indicates boom sizing - very large for GeoSail!
Charging (+ve in sunlight, -ve in eclipse)
  keV e- in tail plasmasheet - high eclipse charging?
  Requires modelling to evaluate
Charging Effects
  Prevent arcing - conducting links around GeoSail
  Charging potential tells us minimum energy measurable for science
Charge/Potential control reduces charge
  Usually required for serious reconnection missions when low energy plasma plays role.
  Scales with area to sun – large mass for GeoSail!
Requires unfeasibly large booms & potential control equipment

## Slide 14: Plasma Environment – Summary
Booms are too long for GeoSail (hundreds of metres)
Potential control is too heavy for GeoSail
GeoSail will not fly potential control instruments or long booms
Aim will be to measure the disturbed plasma with sail
  Comparisons/calibration can be made without sail
  Can be used to deduce environment disturbances by sail
Other options for plasma measurements with sail
  Deconvolve corrupted measurements near sail to estimate plasma properties far from sail
  Compare measurements when sail normal is parallel and perpendicular to velocity vector
Needs detailed modelling to deduce what science can be measured with charged spacecraft!
  Need to assess spacecraft potential in detail for all orbit/plasma phases
  Astrium have carried out preliminary analysis with examples (see next)

## Slide 15: Recent Astrium Plasma Analysis
“First-Look” at GeoSail spacecraft electrostatic charging phenomena & plasma interactions,
  using SPIS (Spacecraft Plasma Interaction System) toolkit
  developed by ONERA/DESP, Artenum & University Paris VII
  See - www.spis.org
Modelled scenarios assess extremes of spacecraft potential around operational orbit
Sphere from sail centre chosen to encompass predicted size of the spacecraft plasma sheath
Simplified geometries used

## Slide 16: Recent Astrium Plasma Analysis (2)
Analysis of charging in representative orbits (sunlight & eclipse)
Useful to assess
  which electron energies can be measured in sunlight, even with sail
  effects of eclipse charging & mitigation
Preliminary results interesting
  Good agreement with NASA L1 analyses
  Geotail results very different - Needs further study
  Results need analysis by scientists to see what can be measured passively, i.e. without long booms & potential control

## Slide 17: Environment – Main Conclusions
Thermal environment critical to platform design
Sail Degradation from Environmental factors:
  combined effect of environments is still a major unknown:
  Needs detailed modelling and testing
Plasmas:
  Debye length very large – unfeasible boom dimensions
  Charging - Common grounding required to minimise arcing.
  Charging - potential control too heavy so will not fly on GeoSail
  GeoSail will therefore measure ‘disturbed’ plasma due to sail
  Further analysis of spacecraft potentials will determine measurement capability
  Detailed EMC (from sail) analysis required
Detailed modelling and testing of environmental effects will predict the design requirements and the measurement limitations of the GeoSail spacecraft

## Slide 18: Environment – Comparions with SPO/IHP
GeoSail generally less challenging (smaller, short mission, static solar distance
GeoSail has some unique challenges:
  Many eclipses (SPO/IHP only have eclipse if planetary flyby)
  High/low power modes; hot/cold cases;
  Wide variety of plasma environments
SPO and IHP challenges:
  possible direct reflections & radiator problems.
  Solar radiation, UV effects will be worse!!! – will impact strongly on sail material degradation
  Debye length will depend on plasma density/velocity – needs characterising
  Potential control more challenging (area >> GeoSail)
GeoSail environment modelling & testing will be directly applicable to the follow-on missions SPO and IHP