## Slide 1: Venus Rendezvous Mission Analysis for Non-perfect Reflecting Solar Sailcraft and Moderate Sail Performance
Chuncheng Wang, Wenhao Huang
(Solar Sailing Group, USTC )

## Slide 2: Solar Sailing Group of USTC (founded in Jan. 2006)
Solar Sailing Group
Hardware
Attitude Control
Trajectory/Orbit
System Simulation

## Slide 3: Motivation
Venus－ one of our nearby neighbors, yet we know little about it
Sample mission analysis using a solar sailcraft which is close to current sail technology, real sail film, moderate sail performance (characteristic acceleration ≤ 0.5 mm/s/s)
Providing constraints to design of interplanetary solar sailcraft from the perspective of trajectory optimization

## Slide 4: Solar Sail Parameters for our Venus Mission Analysis
A=120m X 120m, surface density=10 g/m2
M=500 kg (payload = 356 kg)
ac=0.26 mm/s2－moderate sail performance
Non-ideal sail film (Al|Cr coated)
Traditional trajectory optimization method－difficult to reach adequate initial guess for this problem →new evolutionary nerocontrol (NC) method is perferred (Dachwald 2004)

## Slide 5: Structure of our adopted Artificial Neural Network (ANN, Dachwald 2004 and references therein)
Number of input neurons: 24
Number of hidden layers: 1
Number of neurons in the hidden layers (1 line per layer): 30
Number of output neurons: 3

## Slide 6: Venus rendezvous mission analysis for 5 different initial NC population (using different seed values for the pseudo-random number generator)
Transfer time T=600, 600, 625, 650, 600 days (<T>=615days), respectively, with maximum dispersion < 8% →our result is close to global optimum.

## Slide 7: Best transfer trajectory and attitude history of steering angles

## Slide 8: Constraint for design of attitude control system
Derived strategy of sail steering angles constraints the control system of solar sail to change clock angle as well as cone angle daily in a complex pattern throughout the flight
Frequent attitude control maneuvers should be carried out as instantaneous as possible, i.e. ad<0.8X10-3 mm/s2 to avoid disturbing forces on accurate trajectory transfer (Dachwald 2004)

## Slide 9: Temperature Evolution of Solar Sail during Flight

## Slide 10: Equilibrium temperature of the sail film during Earth－Venus mission

## Slide 11: Constraints to solar sail film design
Solar sail film suffers multiple sharp temperature gradient →challenge the sail film not to degrade significantly on the mechanical and optical performance
Ground experiment on sail film: should simulate the frequent steep temperature gradient above during the flight

## Slide 12: Summary
Moderate performance solar sail can work effectively in interplanetary missions
Attitude control system of the sailcraft should execute instantaneous action daily
Temperature gradient of solar sail should be included in ground experiment of sail film

## Slide 13: Further Work
We will improve the time resolution to study the structure and evolution of temperature gradient in more details
Explore the possibility of solar sail +EP propulsion and related interplanetary trajectory optimization → higher mission feasibility in outer solar system

## Slide 14: Thanks for attention!