## Slide 1: Attitude Control of Solar Sail Spacecraft Based On Rigid Structure Coupled with Flexible Modes
Wang Yong, Zhang Yang, Zhang Guo-qing, Liang Qing
Department of Automation
University of Science and Technology of China
June 29,2007

## Slide 2: Outline
Brief introduction on our research group
Introduction on dynamic models for attitude control of Solar Sail
  General rigid model
  More essential characteristic
Our work on modeling and attitude control of Solar Sail
  Rigid body coupled with flexible modes
  Robust Control Strategy
Conclusions and Next work

## Slide 3: Introduction of Our Research Group －Laboratory of Vibration Control and Vehicle Control
Research Directions:
  Navigation, Guidance and Control of Aerocrafts
  Active Vibration Control of flexible structures
Solar Sail Research Group –cooperating with Pro. Huang Wen-hao
  Research on: Deployment Control and Attitude Control of Solar Sail

## Slide 4: Two types of configurations of Solar Sails
The configuration is proposed by
NASA In-Space Propulsion office (ISP).

## Slide 5: Two types of configurations of Solar Sails
The configuration is proposed by
German Aerospace Center (DLR).

## Slide 6: General Rigid Model of Solar Sail
Based on the latter configuration presented by DLR, Professor Bong Wie formulated rigid dynamic model of Solar Sail [1] .
Linear state space model for control design:
Overall control system is named Gimbaled Thruster Vector Control (TVC) system.

## Slide 7: Main Characteristics of Solar Sails
Large Size and Extreme Flexibility
Data from New Millennium Program Space Technology 7 (NMP ST7 ) proposed by JPL:
  Sail area 1400 m2
  Areal density 0.111 kg/m2
  Sail film thickness 7.5 microns

## Slide 8: More essential characteristic
Dynamics of solar sail is dominated by the flexible structure.
Vibrations of flexible modes are likely to be excited.
Extreme flexibility of solar sail has prominently effect on attitude control of solar sail.

## Slide 9: Our Work on Modeling of Solar Sail
Natural idea: Rigid-body coupled with flexible modes
Realization method: Mixed-coordinates equations-Normalized dynamic equations by combining Euler parameter coordinates with flexible modes coordinates.
General expression:
p－Coupling coefficients
q－Flexible modes coordinates
－Attitude angle

## Slide 10: Pitch-axis Control Model of Solar Sail
Simplified model from configuration of Solar Sail proposed by DLR.

## Slide 11: Flexible modes
Results derived from Dr. Michele Basso and Dr. Max Rotunno with a Finite Element analysis method [3] :
Mode | Coupling coefficients | Modal damping | Modal frequency ( rad /s)
1 | 54.4 | 5.5×10-4 | 0.41
2 | 12.4 | 6.2×10-4 | 0.51

## Slide 12: Model of Rigid-body coupled with flexible modes
Linear state space model for attitude control with state variables

## Slide 13: Robust Control Strategy for Attitude Control
Unneglectable effects of flexible modes on rigid body require robust control strategy to maintain the optimal attitude angle of Solar Sail.
Controller design technique: Robust H∞ control.
General description:
Minimize the cost: ||Twz||∞
G
K
w
z
u
y

## Slide 14: Overall control system
We and Wu are weighting functions in order to penalize the error signal, and control signal respectively.
We1=50× (s+5)/(s+0.01), We2=15, We3=10 and Wu=0.01.
e1
Control system designed by H∞ Control technique
e2
e1
Controller
Plant
r
u
z
We3
Wu
We2
We1
-
e3

## Slide 15: Controller Design
Controller designed by Robust H∞ control technique as follows:

## Slide 16: Simulation results－Optimal Pitch Angle
Figure 2
Control Object: Robustly and Asymptotically Tracking Optimal Pitch Angel 35°
Figure 1

## Slide 17: Simulation results－ Responses of Flexible modes
With robust control strategy, responses of flexible modes are stable ultimately with steady values approach zero.

## Slide 18: Conclusions
Impacts of vibrations of flexible modes on solar sail are lasting and severe.
It’s essential to suppress the vibrations due to flexible modes.
Effectiveness and practicality of a robust control law are demonstrated.
Piezoelectricity film sensors are selected to accomplish the measurements of flexible vibrations, as a result of their low consumption of electric power and their compatibility with the sail.

## Slide 19: Next work
On account of more flexible modes, combination of various control techniques is to be considered to maintain the attitude angle accurate and to suppress vibrations.
More research work on attitude control of solar sail can be done in the presence of disturbances such as solar pressure torque and gravity-gradient torque effects.
A complete three-axis simulation validation of a robust control strategy needs to be performed.

## Slide 20: Reference
[1] Bong Wie, Solar Sail Attitude Control and Dynamics, Part II. Journal of Guidance, Control, and Dynamics. Vol. 27, No.4, 2004: 536—544.
[2] Bong Wie, Solar Sail Attitude Control and Dynamics, Part I. Journal of Guidance, Control, and Dynamics. Vol. 27, No.4, 2004: 526—535.
[3] Michele Basso and Max Rotunno, Robust Attitude Orbit Control for Large Flimsy Appendages, proceedings of the 43rd IEEE Conference on Decision and Control, Bahamas, 2004: 278—283.
[4] Ping Guan, Xiang-Jie Liu, Ji-Zhen Liu, Adaptive fuzzy sliding mode control for flexible satellite, Engineering Applications of Artificial Intelligence 18 (2005) 451–459.
[5] Ren-Wei Zhang, Attitude dynamics and control of satellite orbiting, Beijing University of Aeronautics and Astronautics Publishing Company, 1998, Chapter 9(in Chinese).

## Slide 21
Thanks!
Welcome your questions